# Accessibility Audit: Water point

The purpose of the audit is to examine a water facility, and

- Find out if a physically vulnerable person is able to use the facility independently.

- Identify which features make it easy to use, and which features make it difficult to use by a physically vulnerable person.

- Make suggestions for changes/improvements.

## A.	Allocation of tasks

Appoint a co-ordinator (if you haven’t already). Assign or ask for volunteers for relevant recording tasks: note-taker, measuring dimensions, drawing diagrams, taking photographs, etc. (Team members may do more than one task).

| Names of team members | Equipment needed |
| --- | --- |
| Co-ordinator | Note-book & pen |
| Interviewer | Note-book & pen |
| Note-taker: | Note-book & pen |
| Measurer: | Tape measure |
| Drawer of diagrams: | Note-book & pencil, eraser |
| Photographer: | Camera |

## 2.	Water point - general details

- Type of water point  …………………………………………………………………………………..

- Location /Address …………………………………………………………………………………….

………………………………………………………………………………………………………….......

- Name of implementing organisation/individual……………………………………………………

- Accommodation: ( owned  ( rented 	( other (specify)………………………………..

- Geographic location: ( rural   ( urban   ( peri-urban	( village ( farm ( flat  ( hilly ( (Please describe) ………………………………………………………………………..

- General description of water point, including materials, technology used. ………………………………………………………………………………………………………….....

………………………………………………………………………………………………………….....

………………………………………………………………………………………………………….....

- Draw a diagram (on a separate sheet), a) from above and b) from the side, to show dimensions of the facility and surround.

## C.	Accessibility

Different users now attempt to use the water point. Make a note of who can use it and who cannot, and what features make it difficult to use. Use the attached checklist to remind you of the kind of features to look for, ignore any that are not relevant, and add things that are missing.

- Getting there: …………………………………………………………………………..…………....

………………………………………………………………………………………………………….......

………………………………………………………………………………………………………….......

………………………………………………………………………………………………………….......

Suggested changes: ………………………………………………………………………………………

……………………………………………………………………………………………………………….

……………………………………………………………………………………………………………….

……………………………………………………………………………………………………………….

Checklist Distance: How far is it from home(s)/classroom to water point? Access route: Is the route outside or inside? If used at night, is the path lit? What is the path/ access route made of? Is the path wide enough for all users? (recommended minimum width 90cm). Is the path level and firm, with nothing to trip up? Is the surface of the path slippery when either dry or wet? Are there obstacles that make it difficult to get past, or easy to trip up, especially for visually impaired people? (e.g. vegetation, rubbish, up to 2m above floor level) Are there landmarks that a blind/visually impaired person can follow, e.g. clear surface texture, landmarks or guide rail? If there is a slope or ramp, how steep is it? (Recommended maximum 1 in 10). Is the surface of the slope slippery or non-slip?

- Getting in/on: …………………………………………………………………………………….....

…………………………………………………………………………………………………………......

…………………………………………………………………………………………………………......

…………………………………………………………………………………………………………......

…………………………………………………………………………………………………………......

Suggested changes: ………………………………………………………………………………………

……………………………………………………………………………………………………………….

……………………………………………………………………………………………………………….

……………………………………………………………………………………………………………….

Checklist If there are steps, are they a height that disabled/ elderly people can manage? (recommended max 15 – 17 cm each step). Are the steps even or uneven, firm or broken, non-slip or slippery? Is there a hand-rail for support? What is the difference in height between surrounding area and platform/ apron? Can a wheelchair or crutch user easily enter/ get on? If there is a door or gate, does it open inwards or outwards? How easy is it to unlock and open the door/ gate? e.g. by someone with weak grip? If there is an entrance, is it wide enough for a wheelchair user to enter? (recommended minimum width 80cm)

- Usability: ………………………………………………………………………………………….....

………………………………………………………………………………………………………….......

………………………………………………………………………………………………………….......

………………………………………………………………………………………………………….......

Suggested changes: ………………………………………………………………………………………

……………………………………………………………………………………………………………….

……………………………………………………………………………………………………………….

………………………………………………………………………………………………………….......

Checklist What is the floor made of? Is the floor even, or uneven, firm or unstable, slippery or non-slip? If there is a concrete surround/ apron, measure the dimensions (width – side to side, length front to back). Can the user get close enough to use the water point? Is there a flat platform for the user to sit or stand whilst drawing water? Is there something for the user to lean on while drawing water? Can the user easily reach the operating mechanism (handle/ tap/ rope/ water surface )? If not why not? Is there a place to stand the water container? Can the user easily lift the filled water container and carry it?

## D	Interviews

- Who uses the facility?

…………………………………………………………………………………………………………..

…………………………………………………………………………………………………………..

…………………………………………………………………………………………………………..

- Can they use it easily?

…………………………………………………………………………………………………………..

……………………………………………………………………………………………………………….

……………………………………………………………………………………………………..

Are there people who would like to use it but cannot, or have difficulty? …………………………………………………………………………………………………………..

…………………………………………………………………………………………………………..

…………………………………………………………………………………………………………..

- Please add any additional information or comments.

# Footnotes

This might be a frail elderly woman or man, a small child, a heavily pregnant woman, a wheelchair user or person with difficulty walking, someone who is visually impaired, with weak grip, a broken leg, a limb amputation, the list is endless.

See Jones & Reed (2005, p.48-49) for ramp gradients and lengths.